## Slide 1: Introduction to Operating Systems CS 1550
Process Synchronization - 1
Spring 2023
Sherif Khattab
ksm73@pitt.edu
(Some slides are from Silberschatz, Galvin and Gagne ©2013)

## Slide 2: Announcements
Homework 1 is due next Monday at 11:59 pm
Recitations started last week
  Please watch the videos
Lab 1 is due on 2/4 at 11:59 pm
  Distributed using GitHub Classroom
  Explained in this week’s recitations
Steps of a syscall posted on Canvas
TA Office hours available on the syllabus page
Muddiest points will be anonymous and not seen to students

## Slide 3: Muddiest Points
storage/access of the mode bits
syscalls
  idt/isr vs syscall table
  Difference between f1~f7(what to call them?) and f8~f10(syscall functions)
  the beginning of the syscall process
  syscall steps
  eax register relevance to interrupts/syscall
  How user programs need to be changed for new syscalls
  How high level code interacts with syscalls
xv6 walkthrough
  Array of functions syntax in C
monolithic vs micro

## Slide 4: Problem: race conditions
R is a CPU register
X is a variable stored in memory
R <= x
R = R+1
R => x
R <= x
R = R+1
R => x
P1
x++
x=3
x=5
R <= x
R = R+1
R => x
R <= x
R = R+1
R => x
x=6!
P2
x++

## Slide 5: Race conditions
Cooperating processes share storage (memory)
Both may read and write the shared memory
Problem: can’t guarantee that read followed by write is atomic
  Atomic means uninterruptible
  Ordering matters!
This can result in erroneous results!
We need to eliminate race conditions…

## Slide 6: Atomic operations
If done in one instruction, then not interruptible

## Slide 7: Context Switching
How did the CPU switch from P1 to P2 then to P1 then to P2 again …?

## Slide 8: Process Control Block
  ``Active entities are data structures when viewed from a lower level.’’
  Raphael Finkel, University of Kentucky

## Slide 9: Process Control Block (PCB)
Information associated with each process
(also called task control block)
Process state – running, waiting, etc
Program counter – location of instruction to execute next
CPU registers – contents of all process-centric registers
CPU scheduling information- priorities, scheduling queue pointers
Memory-management information – memory allocated to the process
Accounting information – CPU used, clock time elapsed since start, time limits
I/O status information – I/O devices allocated to process, list of open files

## Slide 10: Process Representation in Linux
Represented by the C structure task_struct
pid_t pid; /* process identifier */ long state; /* state of the process */ unsigned int time_slice /* scheduling information */ struct task_struct *parent; /* this process’s parent */ struct list_head children; /* this process’s children */ struct files_struct *files; /* list of open files */ struct mm_struct *mm; /* address space of this process */

## Slide 11: Context Switch
When CPU switches to another process, the system must save the state of the old process and load the saved state for the new process via a context switch
Context of a process represented in the PCB
Context-switch time is overhead; the system does no useful work while switching
  The more complex the OS and the PCB  the longer the context switch
Time dependent on hardware support
  Some hardware provides multiple sets of registers per CPU  multiple contexts loaded at once

## Slide 12: Context Switching

## Slide 13: Xv6 Code Walkthrough
PCB and process table
Context switching
Calling of the swtch routine

## Slide 14: Context Switching in Xv6
Memory
PCB of Process
PCB of Process
Stack of Process
Stack of Process
context
CPU
%esp
%eip
context
Return address
%eax
%edx
Return address
Return address

## Slide 15: Critical regions
Back to the race conditions problem
Use critical regions to provide mutual exclusion and help fix race conditions
Let’s put the statement x++ in a critical region
Process P1
Process P2
P2 blocked
P1 enters critical region
P2 tries to enter critical region
P2 enters critical region
P1 leaves critical region
P2 leaves critical region
Time

## Slide 16: How to implement critical regions?
Turn-based solutions
Spinlocks
Semaphores
Monitors

## Slide 17: Using Spinlocks
Code for process Pi
While(1){
  Lock(lock)
  // critical section
  Unlock(lock);
  // remainder of code
  }
}
Spinlock lock;

## Slide 18: Spinlock implementation (1/2)
Solution: use hardware
Several hardware methods
  Test & set: test a variable and set it in one instruction
  Atomic swap: switch register & memory in one instruction
  Turn off interrupts: process won’t be switched out unless it asks to be suspended
The first two methods can be implemented in user land
  Why can’t we implement the third method in user land?